## Slide 1: Papers
Divya Khanure (DXK210081)

## Slide 2: ACM Transaction on Networking 2022
Multi-Associated Parameters Aggregation-Based Routing and Resources Allocation in Multi-Core Elastic Optical Networks
  Goal - Reduce blocking probability and resource fragmentation, and thus increase resource utilization.
  Challenges – Mutual restraint relationship, excessive consideration of certain factors causes deterioration of other factors.
  Approach – Use of self-organizing feature mapping (SOFM) model to process multi-dimensional data with relevant features. Routing, core, and spectrum allocation are decided based on the core with higher transmission quality, and then the available slots are classified based on smaller crosstalk in a given direction.

## Slide 3: Multi-Associated Parameters Aggregation-Based Routing and Resources Allocation in Multi-Core Elastic Optical Networks
Parameters for consideration -
  Link length
  Available bandwidth
  Physical layer impairments
  Complex crosstalk
  Multi-dimensional fragmentation
Requirements for consideration –
  Blocking probability
  Link transmission quality/Quality of service (with priority)
Constraints for consideration –
  Continuity
  Contiguity
  Non-overlapping
  Crosstalk
  Spectrum usage

## Slide 4: Multi-Associated Parameters Aggregation-Based Routing and Resources Allocation in Multi-Core Elastic Optical Networks
  Physical Layer Impairments –
    signal transmission direction will also interfere with the crosstalk evaluation model.
    crosstalk models of co-directional transmission and non-directional transmission are slightly different.
    Crosstalk Estimation Along Links:
      nc = no.of adjacent cores
      L = transmission length
      h = average increase in crosstalk per unit length
      that depends on the coupling coefficient,
      bend radius, propagation constant, and core-pitch

## Slide 5: Multi-Associated Parameters Aggregation-Based Routing and Resources Allocation in Multi-Core Elastic Optical Networks
  Physical Layer Impairments –
    Crosstalk Estimation Along Links:
    Compute crosstalk for the same direction and opposite direction.
    Compute wavelength.

## Slide 6: Multi-Associated Parameters Aggregation-Based Routing and Resources Allocation in Multi-Core Elastic Optical Networks
  Physical Layer Impairments –
    Physical Impairments Consideration
      The amplified spontaneous emission (ASE), cross-phase modulation (XPM), and four-wave mixing (FWM) are used for the computation of linear and non-linear impairments.
      Q-factor is used for the Quality of transmission estimation for BER given by
        For OOK channels, the Q-factor is related with the receiver sensitivity and the signal-to noise ratio (SNR) per symbol.
        for QPSK channels, the Q-factor estimation will be complex, and it is also closely related to the self-phase modulation (SPM) and XPM.

## Slide 7: Multi-Associated Parameters Aggregation-Based Routing and Resources Allocation in Multi-Core Elastic Optical Networks
  Multi-Dimensional Resource Fragmentation
    Three dimensions that are considered are link, core, and frequency.
    For a core on a certain link, if at the moment, some continuous spectrum blocks are unavailable it’s treated as multi-dimensional fragments and is computed as fragmentation degree given as:
    where FBfra = fragmented frequency block
    FStotal = total number of Frequency Slot

## Slide 8: Multi-Associated Parameters Aggregation-Based Routing and Resources Allocation in Multi-Core Elastic Optical Networks
  Routing and spectrum assignment algorithm based on SOFM:
    Typical SOFM Model - The SOFM network has two layers and each neuron in the input layer collects external information from each neuron in the output layer through a fully connected weight layer.
      the winning neuron in the output layer and its surro-
      unding neurons need to adjust the weight vector.
      Training - First, initialize parameters including weight
      vector, learning rate, an initial winning neighborhood
      Then, input samples to find the winning neuron and
      update the weight vector. If the learning rate is zero,
      the training ends.
    In MC-EONs, each factor collected from the core level
    can be used as a dimension to be input into SOFM
    model, and finally, the reordered cores along each
    link will be output.

## Slide 9: Multi-Associated Parameters Aggregation-Based Routing and Resources Allocation in Multi-Core Elastic Optical Networks
  Routing and spectrum assignment algorithm based on SOFM:
    Link Quality Assessment Based on SOFM From Core Level –
      Routing model will output k shortest paths for the new service.
      Evaluate the impact of multiple parameters in each core Cj along each link li of each path Lp to form a core attribute set.
      input this set into the SOFM model to obtain the reordered core set along li of Lp.
      This output set will be used as a reference for resource allocation to obtain a CSA solution for each service.

## Slide 10: Multi-Associated Parameters Aggregation-Based Routing and Resources Allocation in Multi-Core Elastic Optical Networks
  Routing and spectrum assignment algorithm based on SOFM:
    Link Quality Assessment Based on SOFM From Core Level –
      For a TA-MCF network –
        7 cores are deployed
        Input - The service S has service index, the source node, destination node, crosstalk threshold which is determined by the selected modulation format, and number of slots consistent with the service bandwidth requirement.
        Output - The Link L has link length, selected core, number of services carried in selected core, available bandwidth, resource utilization, crosstalk and BER evaluation, and fragmentation degree.

## Slide 11: Multi-Associated Parameters Aggregation-Based Routing and Resources Allocation in Multi-Core Elastic Optical Networks
  Routing and spectrum assignment algorithm based on SOFM:
    RCSA Based on LQA-SOFM –
      Step 1: Routing process - When new services arrive at the network, calculate k shortest paths for Service S.
      Step 2: Core selection process - Multi-parameter evaluation is performed for each core Cj on each link Li of each candidate path. The reordered output of SOFM of the core level for each link is taken.
      Step 3: Spectrum assignment process – For each link, li of each candidate path, the free slot blocks in Cj are classified in ascending order of the number of adjacent cores labeled as nc. The slot block with the smallest nc will be preferred.
      Step 4: Reclassify the free slot blocks in the selected class with smaller nc by the number of adjacent cores with the same and opposite directions indicated as n1 and n2
      Select a spectrum and calculate the actual crosstalk and Q values for the new service S. If they meet the requirement, the new service will be served successfully.

## Slide 12: Multi-Associated Parameters Aggregation-Based Routing and Resources Allocation in Multi-Core Elastic Optical Networks
  Experimental setup
    Data plane - software-defined core cross-connect (SD-CXC) node model based on the core selective switch developed with OpenFlow agent.
    All nodes are implemented by virtual machines.
    All links are virtualized and equipped with 7-core fibers with available 358 slots for each core.
    Control plane - transport controller is developed by the Boron version of OpenDaylight.
    Application plane - service generator dynamically generates service sequences with different bandwidth granularities including 10 or 40 Gb/s

## Slide 13: Multi-Associated Parameters Aggregation-Based Routing and Resources Allocation in Multi-Core Elastic Optical Networks
  Compared algorithms
    KSP: k shortest path
    KSP-FF: KSP first fit
    KSP-FF-SC: KSP-FF-spectrum classification
    KSP-NC-FF: KSP-Nonadjacent core-FF
    KSP-SOFM-FF: KSP-Self organizing feature
      mapping – FF
    LQA-SOFM-RCSA: Link quality assessment
    - SOFM - RCSA

## Slide 14: Multi-Associated Parameters Aggregation-Based Routing and Resources Allocation in Multi-Core Elastic Optical Networks
  Performance Evaluation
    Blocking Probability: in terms of SBR and BBR

## Slide 15: Multi-Associated Parameters Aggregation-Based Routing and Resources Allocation in Multi-Core Elastic Optical Networks
  Performance Evaluation
    2. Fragmentation Degree:

## Slide 16: Multi-Associated Parameters Aggregation-Based Routing and Resources Allocation in Multi-Core Elastic Optical Networks
  Performance Evaluation
    3. Resource Utilization:

## Slide 17: Multi-Associated Parameters Aggregation-Based Routing and Resources Allocation in Multi-Core Elastic Optical Networks
  Performance Evaluation
    RCSA scheme in [45] only starts from the path dimension and selects the path with better transmission quality.
    KSP- SOFM-FF only selects cores with better transmission quality in the core dimension but still exploits the FF method in the spectrum dimension.
    KSP-FF-SC uses secondary classification in the spectrum dimension, the FF method is still used for core selection.
    The proposed algorithm considers all the features making it a 3-dimensional approach, against the above-mentioned algorithms that are 1-dimensional as they consider only a single feature.