## Slide 1: Summer 2024 Presentations

## Slide 2: Index
Waypoint Routing in Special Networks
Crosstalk-Avoid Virtual Optical Network Embedding Over Elastic Optical Networks With Heterogeneous Multi-Core Fibers

## Slide 3: 2018 IFIP Networking Conference
Waypoint Routing in Special Networks
  traffic is steered through one or multiple so-called waypoints along the route from source to destination
  Evaluation of complexity of waypoint routing on special networks
  family of outerplanar networks, which have a treewidth of at most two
  Proof for NP-hardness on graphs of treewidth three
  For arbitrary numbers of waypoints, the constraint of different flow sizes between waypoints turns the problem hard

## Slide 4: Waypoint Routing in Special Networks
Solid lines, length = 5 + 3 = 8
Dotted lines, length = 2 + 2 = 4
Waypoint = x – no disjoint path
Solid red - violate unit capacity constraints
source s to the destination t via the waypoint w

## Slide 5: Waypoint Routing in Special Networks
The waypoints depend on each other and must be traversed in a pre-determined order
A Single Waypoint:
    shortest paths (SPs) P1 = SP(s,w) and P2 = SP(w,t) in a greedy fashion is sufficient
One waypoint: greedy is optimal

## Slide 6: Waypoint Routing in Special Networks
Two waypoints: can be infeasible!
Order: s – w1 – w2 – t
the link from w2 to w1 must be used twice.

## Slide 7: Waypoint Routing in Special Networks
Types of graphs are outerplanar and cactus graphs:
  Outerplanar: if it has a planar drawing s.t. all vertices are on the outer face of the drawing
  cactus graph: if any two simple cycles share at most one node (every cactus graph is outerplanar)
link-disjoint path problem to BWRP with unit capacities:
  Set s1 = s, t1 = w1, s2 = w1, t2 = w2, ...,
  a k+1 link-disjoint path algorithm solves unit capacity BWRP for k waypoints.
  Feasible solutions for BWRP can be computed in polynomial time.

## Slide 8: Waypoint Routing in Special Networks
Undirected Outerplanar Graphs
  Let I be the class of undirected WRP with
    1) the graph G is planar
    2) the maximum capacity is cmax, w.l.o.g. n ≥ cmax ∈ N,
    3) s, t and all waypoints touch the outer face F of G,
    4) for every node v ̸∈ F, Σe: {u,v}∈E(G)c(e) is even
  the waypoint routing problem is decidable in time O(n2)
  construction obtainable in time O(n2 · min {n2 , c2max} )
Notes: The input graph is planar,
all terminal pairs touch the outer face,
the degree of every node not on the outer face is even.

## Slide 9: Waypoint Routing in Special Networks
Bidirected Cactus Graphs
  BWRP is optimally solvable in polynomial time on cactus graphs with constant capacity
permutationw1w2w3w4w5.
permutation reduces to w′w2w3
permutation is w1w2′ w3′ w4w5
Notes: shrink the cactus graph down to a tree,
see if for the relevant subset of waypoints (to be described shortly) the feasibility holds on that tree,
reincorporate the excluded rings and find the optimal choice of path segments within each ring, and
construct an optimal route by stitching together the sub-routes obtained from the tree and the segments from each ring.

## Slide 10: Waypoint Routing in Special Networks
Hardness:
  large graph family of treewidth at most 2, the outerplanar graphs the routing paths can be computed efficiently on undirected graphs
  graphs of treewidth 3 - NP-hard in general
  routing through an arbitrary number of waypoints on undirected graphs of treewidth at most 3 is strongly NP-complete
  undirected unicyclic graphs with not flow-conserving waypoints computing a route is weakly NP-complete
  Solving Bidirectional Waypoint Routing Problem optimally is NP-hard

## Slide 11: 2022 Journal of Lightwave Technology
Crosstalk-Avoid Virtual Optical Network Embedding Over Elastic Optical Networks With Heterogeneous Multi-Core Fibers
  both flexible bandwidth allocation and dynamic services deployment encounter a bottleneck when huge volumes of access data are flooded
  Solution - virtual optical network embedding (VONE) over the space division multiplexing (SDM) based elastic optical network (EON) using multi-core fiber (MCF)
  The inter-core crosstalk (IC-XT) can be significantly reduced when virtual networks are embedded over EONs with heterogenous MCF (HMCF).

## Slide 12: Crosstalk-Avoid Virtual Optical Network Embedding Over Elastic Optical Networks With Heterogeneous Multi-Core Fibers
Inter-core Crosstalk

## Slide 13: Crosstalk-Avoid Virtual Optical Network Embedding Over Elastic Optical Networks With Heterogeneous Multi-Core Fibers
Contributions of this paper:
  HMCF structure used in the substrate EONs for the VONE to reduce IC-XT
  The VONE problem is NP-Hard, ILP models embedding solution are the bounds of our proposed heuristic algorithm.
  Proposed algorithm combines the advantages of the two IC- XT suppression approaches, which improve the available frequency ratio and reduce the fragmentation ratio.

## Slide 14: Crosstalk-Avoid Virtual Optical Network Embedding Over Elastic Optical Networks With Heterogeneous Multi-Core Fibers

## Slide 15: Crosstalk-Avoid Virtual Optical Network Embedding Over Elastic Optical Networks With Heterogeneous Multi-Core Fibers
Problem Formulation:
  Objective Function
  Node Embedding Constraints
Notes: most efficient spectrum utilization of embedding all requested service requests.
Equation (2) describes that each node in the topology of a service request should be only embedded into one node of the substrate network. Equation (3) indicates that each node of the substrate network could accept one node in the topology of a service request at most.
Equation (4) guarantees that an embedded substrate node has enough computing capacity to accommodate embedded requested computing resources.

## Slide 16: Crosstalk-Avoid Virtual Optical Network Embedding Over Elastic Optical Networks With Heterogeneous Multi-Core Fibers
Link Mapping Constraints
Core Assigning Constraint
Notes: each link in the topology of a service request should be only embedded into one direction of a lightpath between two nodes in the substrate network, namely, the link-disjoint principle, as describes in (5)
Equation (6) is the flow conservation constraint, which ensures that the total number of the in-flows equals that of the out-flows on all substrate nodes except for the embedded source and destination substrate node.
Equation (7) describes that each service request selects only a core on each link of the lightpath established by (5) and (6).

## Slide 17: Crosstalk-Avoid Virtual Optical Network Embedding Over Elastic Optical Networks With Heterogeneous Multi-Core Fibers
Frequency Slots Allocating Constraints
Notes: 8. No overlapping constraints
9. IC-XT-avoid constraint
10. maximum index of the frequency slots ie frequency continuity
11. frequency slots capacity

## Slide 18: Crosstalk-Avoid Virtual Optical Network Embedding Over Elastic Optical Networks With Heterogeneous Multi-Core Fibers
NP- hard for all 4 following:
  VONE over EONs with MCF with the IC-XT (VMXT)
  VONE over EONs with MCF avoiding the IC-XT (VMXTA)
  VONE over EONs with HMCF with the IC-XT (VHXT)
  VONE over EONs with HMCF avoiding the IC-XT (VHXTA)

## Slide 19: Crosstalk-Avoid Virtual Optical Network Embedding Over Elastic Optical Networks With Heterogeneous Multi-Core Fibers
Heuristic Algorithm
  Predefined Core Prioritization
    smaller index in Core_Priority, the higher priority of the element, ie service request will be assigned preferentially
    core priority order is 1 → 3 → 2 → 5 → 4
  Core classification algorithm
    different types of service requests are
    assigned between adjacent cores, which
    avoids the IC-XT.

## Slide 20: Crosstalk-Avoid Virtual Optical Network Embedding Over Elastic Optical Networks With Heterogeneous Multi-Core Fibers

## Slide 21: Crosstalk-Avoid Virtual Optical Network Embedding Over Elastic Optical Networks With Heterogeneous Multi-Core Fibers
Fragmentation vs No.of Service requests
Crosstalk vs No.of Service requests

## Slide 22: Crosstalk-Avoid Virtual Optical Network Embedding Over Elastic Optical Networks With Heterogeneous Multi-Core Fibers
Frequency Utilization Ratio vs Requests
Available Frequency Ratio vs Requests